Date: 17 May 2010

## Part No.: PT80309

## 0.5MM CU/MICA/LSZH/LSZH/STA/LSZH

## CATEGORY 3 FIRE RESISTANT TELEPHONE CABLE

Application:

This cable is used for medium frequency data or telephone systems, suitable for indoor and outdoor installations.

Construction:

Conductor: 			   Plain Annealed Solid Copper to IEC 228 Class 1

Insulation:  			   Mica tape and LSZH insulation

Shape: 				   Circular

Inner Sheath:          LSZH

Armour:              Steel tape armour

Outer Sheath:		   LSZH

Sheath color:          Black

Voltage Rating:        300/500V

Temperature Rating:   0 ℃ to 40 ℃

Bending Radius:       6 x overall diameter

Marking:  The cable is marked with white or other colors as follows:

- Caledonian Cables Co., Ltd

- Type and size of cable

- Manufacturing date

- Meter Marking

The meter mark is printed every meter with an accuracy of (0.5%.

Other printing is available according to customer request.

Table 1. Technical Data

| Number of Pair | Diameter of Conductor (mm) | Diameter of Cable (mm) |
| --- | --- | --- |
| 50 | 0.5 | 30.0 |

Electrical Properties:

Frequency: 1—16MHz

Characteristic Impedance: 100±15Ω
Nominal Velocity of Propagation： 65%
Maximum DC. Resistance： 9.38Ω/100m
Maximum DC Resistance Unbalance： 5%
Maximum Propagation Delay Skew： 30ns / 100m
Maximum Propagation Delay： 536 ns / 100m @ 100 MHz
Minimum Bending Radius: 10 × cable outer diameter
Voltage Rating： 60V rms
Maximum Pulling Load: 80 N
Working Temperature： (-20) ℃ — (+ 60) ℃

Storage Temperature ： (-5) ℃ — (+50) ℃ 
Flame Retardancy： IEC 332-3A, IEC60331

Table 2. Transmission Parameters

|  | NEXT (db/100m ） Minimum Value/Typical Value/Standard Value ≥ | ATTENUATION (db/100m ） ≤ | SRL (db) Minimum Value/Typical Value/Standard Value ≥ |
| --- | --- | --- | --- |
| 1 | 43.0/48.0/41.0 | 2.6 | 13.0/16.0/12.0 |
| 4 | 34.0/38.0/32.0 | 5.6 | 13.0/16.0/12.0 |
| 8 | 29.0/33.0/26.0 | 8.5 | 13.0/16.0/12.0 |
| 10 | 28.0/33.0/26.0 | 9.8 | 13.0/16.0/12.0 |
| 16 | 25.0/30.0/23.0 | 13.1 | 11.0/14.0/10.0 |

The data included in the present catalogue are merely indicative; Caledonian Cables Limited reserves to itself the right to change them as its own discretion in any time.

# Text boxes

LSZH Outer Jacket

LSZH Inner Jacket

Steel Tape Armour

Mica and LSZH Insulation

Copper Conductor